11B Analysis with S455 Setup
Setup and Detectors
Particle Identification
 12C(p,2p)11B reaction
Summary & Outlook
Tobias Jenegger
R3B Collaboration Meeting
30. Nov. 2020
Supported by BMBF 05P15WOFNA and 05P19WOFN1.
The results presented here are based on the experiment s444/s473, which was performed at the beam line/infrastructure Cave C at the GSI Helmholtzzentrum für Schwerionenforschung, Darmstadt (Germany) in the frame of FAIR Phase-0.
Physics with R3B
CALIFA – Design
TUM Members:
Roman Gernhäuser,Lukas Ponnath,Philipp Klenze,Tobias Jenegger

---
The S455 Setup (February 2020)
GLAD magnet
CALIFA
NeuLAND
R³B Music
MWPC1
neutrons
beam
MWPC0
START
MWPC2
TWIM Music
MWPC3
Daughter
nuclei
Beam energy: from 400 to 800 AMeV
Intensities: 1kHz - 1MHz
Beamtype: 12C,
Target: C, CH2
Time of Flight Wall

---
Particle Identification
START
TWIM Music
x
size*1.5{B %rho = {{%beta %gamma M} over {q}}}
MWPC1
MWPC0
z
Time of Flight Measurement: Start to TOFW
Flight-path Reconstruction: Tracking Detectors (MWPC1, 2 and 3)
Charge Measurement : TWIM Music
CALIFA
MWPC2
MWPC3
Time of Flight Wall
11B Analysis with S455 Setup

---
R3B @ FAIR
Flightpath Reconstruction
Radius Reconstruction:
size*1.5 {R = {L_eff} over {2sin({%theta_"in" + %theta_out} over {2}) } }
Known:
position and inflight angle (θin) before GLAD
position after GLAD (MWPC3)
color blue size*1.5 %theta_{ "in" }
     compute θout iteratively:
MWPC1
MWPC2
MWPC3

---
Charge versus A/q
12C
11C
10B
11B

---
12C(p,2p)11B reaction
p_1( vec p_1 , E_1 )
p( vec p_0 , E_0 )
p( vec p_A, E_a )
p_{A-1}( vec p_{A-1}, E_{A-1} )
p_A + p_T = p_1 + p_2 + p_{A-1} + p_{ %gamma }
p_{%gamma}( vec p_%gamma , E_%gamma )
p_2( vec p _{2} , E_2 )

---
Gamma Spectrum of 11B
Doppler Correction
size*2 E_{ %gamma } = size*2 %gamma size*2E_{ lab} size*2( 1- %beta cos (%theta ))
2.1 MeV (1/2-) p-hole state
5.0 MeV (5/2-) p-hole state

---
Polar Angular Distribution of protons for 12C(p,2p)11B
12C beam
Barrel region with high acceptance
iPhos region
11B Analysis with S455 Setup

---
Arzimuthal Distribution of protons for 12C(p,2p)11B
z
x
y
Psi1 [degreees]
CALIFA left half (90°) iPhos
CALIFA right half (45°) iPhos
11B Analysis with S455 Setup
Tobias Jenegger
Psi2 [degreees]

---
Momentum Distribution 2p & 11B
expected: barrier line
Explanation for smearing needed:
→ use simulation
→boosting to 12C frame:
size *1.5 p_{ 12C } = size*1.5 p_{ i } + size*1.5 p_{11B}
pi
11B
cos( %gamma ) approx 1
size*1.5%gamma
With 5.4 mm carbon target:

---
Summary & Outlook
→ Particle Identification works out
→ Gamma spectrum and angular distribution plots look reasonable
→ Further investigations for momenta distributions of the outgoing particles needed
→ Expand analysis towards 10B isotope
11B Analysis with S455 Setup
Tobias Jenegger

---
Thank you!
CALIFA @ Technical University of Munich (TUM)
Roman Gernhäuser, Lukas Ponnath, Philipp Klenze, Tobias Jenegger
Thank you!

---
Backup